## Slide 1
Learning Objectives
• Understand the Workflow Path
• Use the Project Browser
• Understand the concept of Space
• Specify the space Object Settings
• Work with space styles and tools
• Understand the concept of zones
• Workspace switching in MEP

## Slide 2
Introduction
AutoCAD MEP, a software based on AutoCAD platform, is used to design, draft, and document electrical, mechanical, and piping system of buildings.
The first step while creating such a system is to create a project.
Thereafter drawings are added to this project to represent various components of the building like electrical system, ducts, and so on.
These drawings are then arranged according to the workflow of the project.

## Slide 3
WORKFLOW
Figure 2-1 Workflow for an HVAC system in AutoCAD MEP
Workflow is a sequence of connected steps required to create a specific type of system.
It is dependent on the system to be created.

## Slide 4
Project Browser
Figure 2-3 The Add Project dialog box
Figure 2-2 The Project Browser
The Project Browser is used to manage project files.
A project file contains the record of drawing files related to a category.
Creating a New Project file
A new project file can be created by using the New Project tool available at the bottom left corner of the Project Browser.

## Slide 5
contd.
Figure 2-4 The Select Project dialog box
Figure 2-5 The Select Project dialog box

## Slide 6
Content Browser
Figure 2-6 The Autodesk Content Browser 2016
The Content Browser tool is used to display the Autodesk Content Browser 2015 window related to the currently loaded project.

## Slide 7
Content Browser (contd.)
Figure 2-7 The Autodesk Content Browser displaying component categories

## Slide 8
Content Browser (contd.)
Figure 2-8 Component being placed in the Tool Palettes

## Slide 9
Synchronize Projects
Figure 2-9 The Synchronize Project with Project Standards dialog box
The Synchronize Projects tool is used to synchronize the current project with the AEC project standards.
To synchronize the project , choose the Synchronize Projects tool available at the bottom of the PROJECT NAVIGATOR.

## Slide 10
Configure Project Standards
Figure 2-10 The Configure AEC Project Standards dialog box
The Configure Project Standards tool is used to set up the project standard.
These project standards are used to synchronize the project drawings.
When you choose this tool, the Configure AEC Project Standards dialog box will be displayed.

## Slide 11
Show External References
Figure 2-11 The External References dialog box
The Show External Reference tool is used to display external references for any drawing in the current project.
When you select a drawing in the PROJECT NAVIGATOR and choose this button, the External References dialog box will be displayed.

## Slide 12
Add View
Figure 2-12 The Add General View dialog box
There are three types of views that can be added to the View area: General view, Section/ Elevation view, and Detail view.
The Add View tool is used to add a new view to the View area.

## Slide 13
Add View (Contd.)
Figure 2-13 The Add General View dialog box with the Context page displayed

## Slide 14
Add View (Contd.)
Figure 2-14 The Add General View dialog box with the Content page displayed

## Slide 15
Sheet Tab
Figure 2-15 The PROJECT NAVIGATOR with the Sheets tab chosen
Figure 2-16 The New Sheet dialog box

## Slide 16
STYLES BROWSER
used to import the styles and system definition to current drawing.
You can also override the style or definition of an existing objects in the drawing area by using this palette.
Figure 2-17 The STYLES BROWSER palette

## Slide 17
Create Type
Figure 2-18 The space created by using the Insert option
Figure 2-19 The rectangular space with cursor attached to the corner point of the rectangle
Figure 2-20 The polygon type space created by using arcs
Figure 2-21 The polygon type space created by using lines
SPACE

## Slide 18
Editing Spaces
Figure 2-22 The Space contextual tab
Figure 2-23 The Object Viewer dialog box
perform various editing operations on the created spaces.
When you select a space from the drawing area, the Space contextual tab will be available in the Ribbon.
Object Viewer
The Object Viewer tool is used to display the selected object in a separate 3D preview window.

## Slide 19
Edit Style
Figure 2-24 The Space Style Properties dialog box
This drop-down is available in the General panel of the Space contextual tab in the Ribbon.
The tools in this drop-down are used to modify the style of the space.
By using the options in this dialog box, you can change different properties of the selected space such as length and width of the space, target area, and various offset values.

## Slide 20
Edit Style (Contd.)
Figure 2-25 The Style Manager dialog box

## Slide 21
Edit Style (Contd.)
Figure 2-26 The Style Manager dialog box with theme style options

## Slide 22
Edit Style (Contd.)
Figure 2-27 The Style Manager dialog box with Zone Templates selected

## Slide 23
Tag
Figure 2-28 The Edit Property Set Data dialog box
This tool is used to add a tag to the object.
To add a tag, choose Space > General > Tag from the Ribbon; you will be prompted to select an object on which you want to add a tag.

## Slide 24
Edit in Place
Figure 2-29 The information box showing various editing options
This tool is used to edit an extruded 3D space.
choose Space > Modify > Edit in Place from the Ribbon; the Edit in Place: Space Body Modifier contextual tab will be displayed and the selected space will be converted into a free form space.

## Slide 25
Edit Surfaces
Figure 2-30 Space with editing points
This tool is used to edit only the faces of the space.
Choose Space > Modify > Edit Surfaces from the Ribbon; the selected space will be converted into a free form space.

## Slide 26
Figure 2-31 Space with its vertex attached to the cursor
Edit vertices
This tool is used to add a vertex to the selected edge.
choose Space > Modify > Edit Vertices from the Ribbon; the vertex will be attached to the cursor and you will be prompted to click in the drawing area to add the vertex.

## Slide 27
WORKSPACES
Figure 2-32 The Workspace Switching flyout

## Slide 28
Customize
Figure 2-33 The Customize User Interface dialog box
The Customize tool is used to customize the user interface of AutoCAD MEP.