## Slide 1
Learning Objectives
• Create vertical section of the model
• Create horizontal section of the model
• Create section line for creating section views
• Create elevation line
• Create hidden line projections
• Slice a 3D object for extracting a profile
• Create schedules and tables

## Slide 2
Introduction
Learn to create different views of the building model for representation.
These views represent every minute detail of the building model.

## Slide 3
CREATING VERTICAL SECTIONS
Figure 8-2 The Building Section Line contextual tab
Vertical Section of an object is created by passing a vertical plane through the objects.
To create a section, choose the Vertical Section tool from the Section & Elevation panel of the Home tab in the Ribbon; you will be prompted to specify the start point of the section line.
Figure 8-1 The drawing after creating the section line

## Slide 4
Enable Live Section
This tool is used to create live sections by using the current section line.
This type of section is a dynamic section of the building and gets modified as you modify the section line.
To create a live section, select the section line and then choose the Enable Live Section tool from the Live Section panel of the Building Section Line contextual tab in the Ribbon; the live section will be created.
Figure 8-3 The drawing with live section created

## Slide 5
Figure 8-4 The Generate Section/Elevation dialog box
This tool is used to generate section view of a building with respect to the section line selected.
To generate a section, choose the Generate Section tool from the Modify panel of the Building Section Line contextual tab in the Ribbon; the Generate Section/Elevation dialog box will be displayed.
Generate Section

## Slide 6
Figure 8-5 The 3D section view of the building
This radio button is used for creating 3D section view of the building.
3D Section/Elevation Object

## Slide 7
2D Section/Elevation Object with Hidden Line Removal
Figure 8-6 The drawing after creating 2D section
This radio button is used for creating 2D section view of the building.

## Slide 8
CREATING HORIZONTAL SECTION
The Horizontal Section tool is used to create a section of the building bounded by two horizontal planes.
To create a horizontal section, choose the Horizontal Section tool from the Section & Elevation panel of the Home tab in the Ribbon.
CREATING A SECTION LINE
The Section Line tool is used to create a section line passing through any user defined points.
To create a section line, choose the Section Line tool from the Section & Elevation panel of the Home tab in the Ribbon.

## Slide 9
Figure 8-7 The PROPERTIES palette
CREATING ELEVATION LINE
The Elevation Line tool is used to create an elevation line passing through user defined points.
To create an elevation line, choose the Elevation Line tool from the Section & Elevation panel of the Home tab in the Ribbon.

## Slide 10
Figure 8-8 The model with its hidden line projection
CREATING HIDDEN LINE PROJECTION
The Hidden Line Projection tool is used to create 2D projections with hidden projection lines of the model.
To create the projection, choose the Hidden Line Projection tool from the expanded Section & Elevation panel of the Home tab in the Ribbon.

## Slide 11
Figure 8-9 The model sliced using the Quick Slice tool
The Quick Slice tool is used to extract a polyline outline of the slice created using the model.
SLICING THE MODEL
To extract the outline, choose the Quick Slice tool from the expanded Section & Elevation panel in the Home tab of the Ribbon.

## Slide 12
Figure 8-10 The Batch Refresh 2D Section/Elevations dialog box
The Batch Refresh tool is used to refresh all 2D sections and elevations created in the current project or in the specified folder.
REFRESHING SECTIONS AND ELEVATIONS IN A BATCH
To refresh the 2D sections and elevations, choose the Batch Refresh tool from the expanded Section & Elevation panel of the Home tab in the Ribbon.

## Slide 13
Figure 8-11 The Detail Component Manager dialog box
INSERTING DETAIL COMPONENTS
The detail components are used to represent AutoCAD MEP components with detailed parameters.
To insert detail components, choose the Detail Components tool from the Details panel of the Home tab in the Ribbon.

## Slide 14
Figure 8-12 The Add Group dialog box
This button is available below the Edit Database button and is used to add groups to the database.
Add Group
To add groups, choose the Add Group button; the Add Group dialog box will be displayed.

## Slide 15
Figure 8-13 The New Component dialog box
Add Component
This button is available below the Add Group button and is used to add components to the selected group.
To add a component, choose the Add Component button; the New Component dialog box will be displayed.

## Slide 16
Figure 8-14 The Select Keynote dialog box
Keynote
This edit box is used to assign key notes about the component being created.
You can also assign the key notes by selecting them from the Select Keynote dialog box.
The Select Keynote dialog box will be displayed on choosing the Select Keynote button from the New Components dialog box .

## Slide 17
Figure 8-15 The Select Layer Key dialog box
This field is used to specify a layer key for the current component.
Click on this field; the Select Layer Key dialog box will be displayed.
Layer Key

## Slide 18
Figure 8-16 The Select Block Library dialog box
Block drawing location
The options in this drop-down list are used to select the location of block drawing for the component.
Select the Browse option from the drop-down list to select a block drawing file from a user defined location; the Select Block Library dialog box will be displayed.

## Slide 19
Figure 8-17 The Component Properties dialog box
This tool is available below the Add Component tool.
It is used to edit current component.
To edit the selected component, choose the Edit button; the Component Properties dialog box will be displayed.
Edit

## Slide 20
Figure 8-18 The Air Terminal Devices Schedule
Figure 8-19 The Schedule Table contextual tab
Air Terminal Devices Schedule
This tool is available in the Schedules drop-down in the Annotation panel of the Home tab of the Ribbon when the HVAC option is selected in the Workspace Switching flyout .
To create an air terminal device schedule, choose the Air Terminal Devices Schedule tool from the Schedules drop-down.

## Slide 21
Figure 8-20 The Schedule Table Style Properties dialog box
Edit Style
The tools in this drop-down are used to edit styles and definitions of the schedule tables.
You can also change the text styles and property data formats used in the schedule tables.

## Slide 22
Figure 8-21 The Style Manager displayed on choosing the Schedule Table Styles tool
Schedule Table Style
This tool is used to change the style of the selected schedule table.
To change the style of the selected schedule table, choose the Schedule Table Styles tool from the Edit Style drop-down; the Style Manager dialog box will be displayed.

## Slide 23
Figure 8-22 The Style Manager displayed on choosing the Classification Definitions tool
This tool is used to change the classification style used in the current table.
To change the classification style, choose the Classification Definitions tool from the Edit Style Representation and Schedules 8-23 drop-down; the Style Manager will be displayed.
Classification Definition

## Slide 24
Figure 8-23 The Style Manager displayed on choosing the Property Set Definitions tool
This tool is used to change the definitions of property set for the selected property.
To change the definition of property sets, choose the Property Set Definitions tool from the Edit Style drop-down; the Style Manager will be displayed.
Property Set Definitions

## Slide 25
Figure 8-24 The Style Manager displayed on choosing the Property Data Formats tool
Property Data Formats
This tool is used to change the format data specified in the schedule table.
To change the data format, choose the Property Data Formats tool from the Edit Style drop-down; the Style Manager dialog box will be displayed .

## Slide 26
Figure 8-25 The Text Style dialog box
Text Styles
This tool is used to change the text style in the schedule table.
To change the text style, choose the Text Styles tool from the Edit Style drop-down; the Text Style dialog box will be displayed.

## Slide 27
Figure 8-26 The Schedule Table Style Properties dialog box
This tool is used to copy the style of an existing object and then create a new style based on that style.
To copy a style, choose the Copy Style tool from the General panel of the Schedule table tab; the Schedule Table Style Properties dialog box.
Copy Style

## Slide 28
Figure 8-27 The Insert Table dialog box
Table
The Table tool is available in all the workspaces.
To create a table, choose this tool from the Schedule drop-down in the Annotation panel of the Home tab in the Ribbon; the Insert Table dialog box will be displayed.

## Slide 29
Figure 8-28 The Table Style dialog box
Table style
The options in the Table style drop-down list are used to select a table style for the current table.
You can edit the selected table style by using the options available in the Table Style dialog box.

## Slide 30
Figure 8-29 Partial view of the Table Cell contextual tab
Table Editing
Table editing can be done after selecting the table schedule created by the user.
You can edit a schedule table in the same way as done in an Excel sheet. On selecting a cell from the table, the Table Cell contextual tab will be displayed in the Ribbon.
Figure 8-30 The Insert a Block in a Table Cell dialog box
Insert
The tools available in this panel are used to insert various types of objects in the table.

## Slide 31
Figure 8-31 The Field dialog box
This tool is used to insert a text field in the current cell.
To insert a text field, choose the Field option; the Field dialog box will be displayed.
Field

## Slide 32
Figure 8-32 The Select a Data Link dialog box
Data
The tools in this panel are used to manage data links of the selected cell.
This tool is used to link the selected cell in the table to a field in the excel sheet. To do so, choose the Link Cell tool from the contextual tab; the Select a Data Link dialog box will be displayed.
Link Cell

## Slide 33
Contd.
Figure 8-46 The New Excel Data Link dialog box
Figure 8-47 The New Excel Data Link dialog box