## Slide 1
Learning Objectives
• Understand the use of schematics
• Add schematic symbols to drawings
• Create schematics lines in the drawing
• Display schematic representation of existing drawing

## Slide 2
Introduction
you will learn about various tools that are used for creating a schematic drawing for a building system.
You will also learn the use of equipment and schematic lines in a schematic drawing.

## Slide 3
Schematic Workspace
To invoke this workspace, choose the Schematic option from the Workspace Switching flyout; the Schematic workspace will be activated.
The tools to create a schematic drawing are available in the Build panel of the Home tab in the Ribbon.
Figure 9-1 Partial view of the Ribbon in the Schematic workspace

## Slide 4
Equipment
This tool is available in the Build panel of the Home tab in the Ribbon.
This tool is used to add equipment to the drawing.
To add an equipment, choose the Equipment tool from the Ribbon; the Add Multi-view Parts dialog box will be displayed.
Schematic Symbol
Schematic symbols are the symbolic representations of physical objects required in a building system.
In AutoCAD MEP, there are two types of schematic symbols: In-line symbols and End-of-line symbols.

## Slide 5
To add a schematic symbol, choose the Schematic Symbol tool from the Build panel of the Home tab in the Ribbon; the symbol will get attached to the cursor and you will be prompted to specify the insertion point for the symbol.
PROPERTIES Palette
The options in the PROPERTIES palette are used to change the parameters of the schematic symbols.
Figure 9-2 The PROPERTIES palette displayed on choosing the Schematic Symbol tool

## Slide 6
Description
This field is available in the BASIC > General rollout of the Design tab in the PROPERTIES palette.
Figure 9-3 The Description dialog box
Style
This option is available in the BASIC > General rollout of the PROPERTIES palette.
This option is used to select a schematic symbol from the list of symbols available in AutoCAD MEP.
To select a symbol, choose the Style option from the PROPERTIES palette; the Select Style dialog box will be displayed.

## Slide 7
Figure 9-4 The Select Style dialog box
In this dialog box, the options in the Drawing File drop-down list are used to specify the template file for schematic symbols.

## Slide 8
Schematic Line
Schematic lines are used to represent various types of connections in a building system.
To create a schematic line, choose the Schematic Line tool from the Build panel in the Home tab of the Ribbon; you will be prompted to specify the start point for the schematic line.
Figure 9-5 The PROPERTIES palette displayed on choosing the Schematic Line tool

## Slide 9
Schematic Line Styles
While creating a schematic diagram, you might require to change the style of the schematic lines.
The style of schematic lines can be changed by using the Style Manager.
Figure 9-6 The Style Manager with schematic line styles

## Slide 10
General Tab
Keynote
This edit box is used to specify key notes for the schematic line style.
Figure 9-7 The Select Keynote dialog box
You can enter the desired key notes in the edit box or you can choose the Select Keynote button next to the edit box to select a keynote from the list of predefined keynotes.

## Slide 11
Notes
This button is used to specify notes for the selected line style.
Figure 9-8 The Notes dialog box
To specify the notes, choose the Notes button from the bottom of the General tab; the Notes dialog box will be displayed.
There are two tabs available in this dialog box: Notes and Reference Docs.

## Slide 12
Designations Tab
The options in this tab are used to specify designations for the schematic lines.
Designations are used to create unique IDs for the schematic lines.
Figure 9-9 The Style Manager with the Designations tab chosen

## Slide 13
Annotation Tab
The options in this tab are used to modify annotation style for a schematic line.
Crossings Area
There are three buttons available in this area:
Do Nothing, Overlap Graphics, and Break Existing Line.
Figure 9-10 The Style Manager with the Annotation tab chosen

## Slide 14
Display Properties Tab
The options in this tab are used to modify the display representations of schematic lines.
Figure 9-11 The Style Manager with the Display Properties tab chosen

## Slide 15
Version History Tab
Figure 9-12 The Style Manager with the Version History tab chosen
The options in this tab are used to record the history of the selected line style.

## Slide 16
Schematic Representation of an Existing System
To display the schematic representation,open the desired file and then click on the Level of Details button in the Drawing Status Bar; a flyout will be displayed.
Figure 9-13 The flyout displayed on choosing the Level of Details button

## Slide 17
Figure 9-14 The schematic representation of an HVAC system
Choose the MEP Schematic option from the flyout; the current drawing will be displayed with schematic representations.
Contd.