## Slide 1
Learning Objectives
• Understand the concept of points in Civil 3D
• Create points using different methods
• Create point styles
• Create point label styles
• Understand file formats
• Edit points
Notes: <number>

## Slide 2: POINT OBJECT
Point object represents location in 3D space.
For example trees, road geometry points, property corners and edge of pavements.
Location defined coordinates X, Y and Z.
Point object has two major components, marker and label.
Marker represents the location of the point object. Display controlled by the point style
Point label displays the information about that point object. controlled by the point label style.
Figure 2-1 A point with number, elevation, and description

## Slide 3
Creating Points
Ribbon: Home > Create Ground Data > Points drop-down > Point Creation Tools
Command: CREATEPOINTS
Figure 2-2 The PROPERTIES palette showing different point properties
In Civil 3D, you can create points using three different methods:
  locating points by using the Create Points toolbar
  Importing points from external point files
  converting AutoCAD points into Civil 3D points.
These are divided into six different sub categories

## Slide 4
The Miscellaneous Category
Ribbon: Home > Create Ground Data > Points drop-down >
Create Points-Miscellaneous
Command: CREATEPOINTS
The tools in this category are used to create points by specifying the point location in the drawing manually.
Figure 2-3 Miscellaneous point creation tools

## Slide 5
Manual
Ribbon: Home > Create Ground Data > Points drop-down >
Create- Miscellaneous > Manual
Command: CREATEPOINTMANUAL
Geodetic Direct
Ribbon: Home > Create Ground Data > Points drop-down >
Create- Miscellaneous > Geodetic Direct
Command: CREATEPTGEODETICDIR
Automatic
Ribbon: Home > Create Ground Data > Points drop-down >
Create- Miscellaneous > Automatic
Command: CREATEPOINTAUTOMATIC

## Slide 6
Polyline Vertices - Automatic
Ribbon: Home > Create Ground Data > Points drop-down >
Create- Miscellaneous > Polyline Vertices – Automatic
Command: CREATEPTPLYINCTRVERTAUTO
Polyline Vertices - Manual
Ribbon: Home > Create Ground Data > Points drop-down >
Create- Miscellaneous > Polyline Vertices – Manual
Command: CREATEPTPLYLINECTRVERTMAN

## Slide 7
The Intersections Category
Ribbon: Home > Create Ground Data > Points drop-down >
Create Points-Intersections
Figure 2-4 The tools in the Intersections category

## Slide 8
Direction/Direction
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Intersections > Direction/Direction
Command: CREATEPOINTDIRECTIONDIR
Figure 2-5 The point added at the specified offset distance from the intersection of direction lines of two points

## Slide 9
Distance/Distance
Ribbon: Home > Create Ground Data > Points drop-down >
Create Points- Intersections > Distance/Distance
Command: CREATEPOINTDISTANCEDIST
Figure 2-6 Points created at the intersection of arcs of specified radial distances defined from two points

## Slide 10
Direction/Perpendicular
Ribbon: Home > Create Ground Data > Points drop-down >
Create Points-Intersections > Direction/Perpendicular
Command: CREATEPOINTDIRECTIONPERP
Figure 2-7 The point created in a specified direction, at a perpendicular distance from the specified point
Used to create a point at the intersection of the direction line of a point and the direction line of a point perpendicular to that point.
Specify the start point of the direction (bearing or azimuth).
Specify offset.
Specify location of perpendicular point
Specify point description and elevation

## Slide 11
Distance/Object
Ribbon: Home > Create Ground Data > Points drop-down >
Create Points-Intersections > Distance/Object
Command: CREATEPOINTDISTANCEOBJECT
Figure 2-8 Point created at the intersection of the arc object and the radial distance from a point

## Slide 12
The Alignments Category
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Alignments
Figure 2-9 The flyout displaying tools in the Alignments category

## Slide 13: Station/Offset
Used to create points at specified distance from the selected station in an alignment.
Invoke this tool from the Create Ground Data panel
Select required alignment.
Select the station at which you want to create a point
Specify the offset, description and elevation of the point when prompted.
The point will be created and displayed at the specified offset distance from the selected station.
This tool is useful for creating points for Right of Way, lanes, and shoulders.
Ribbon: Home > Create Ground Data > Points drop-down > Create Points – Alignments > Station/Offset
Command: CREATEPOINTSTATIONOFFSET

## Slide 14
Measure Alignment
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Alignments > Measure Alignment
Command: CREATEPOINTMEASUREALIGN
At Alignment Geometry
Ribbon: Home > Create Ground Data > Points drop-down >
Create Points – Alignments > At Alignment Geometry
Command: CREATEPOINTATPTPCSCETC
Import from File
Ribbon: Home > Create Ground Data > Points drop-down > Create Points- Alignments > Import from File
Command: CREATEPOINTIMPORTFROMFILE
Figure 2-10 The Enter file format dynamic input prompt

## Slide 15
The Surface Category
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Surface
Random Points
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Surface > Random Points
Command: CREATEPOINTRANDOMPOINTS
Figure 2-11 The fly-out displaying tools in the Surface category

## Slide 16
Figure 2-12 The points added at the surface elevation
Along Polyline/Contour
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Surface > Along Polyline/Contour
Command: CREATEPOINTALONGPOLYCONTOUR
On Grid
Ribbon: Home > Create Ground Data > Points drop-down> Create Points - Surface > On Grid
Command: CREATEPOINTONGRID

## Slide 17
The Interpolate Category
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Interpolate
Interpolate
Ribbon: Home > Create Ground Data > Points drop-down > Create Points – Interpolate > Interpolate
Command: CREATEPOINTINTERPOLATE
By Relative Location
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Interpolate > By Relative Location
Command: CREATEPOINTBYRELLOCATION
Figure 2-13 The fly-out displaying tools in the Interpolate category

## Slide 18
Intersection
Ribbon: Home > Create Ground Data > Points drop-down > Create Points – Interpolate > Intersection
Command: CREATEPTINTERPOLINTERSEC
Figure 2-14 The interpolated points created at the intersection

## Slide 19
The Slope Category
High/Low Point
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Slope > High/Low Point
Command: CREATEPOINTHIGHLOWPOINT
Figure 2-15 The flyout displaying tools in the Slope category
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Slope
Figure 2-16 Point created at the intersection of slopes

## Slide 20
Slope/Grade-Distance
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Slope > Slope/Grade – Distance
Command: CREATEPOINTSLOPEGRADEDIST
Slope/Grade Elevation
Ribbon: Home > Create Ground Data > Points drop-down > Create Points - Slope > Slope/Grade – Elevation
Command: CREATEPOINTSLOPEGRADEELEV

## Slide 21
Figure 2-17 The Import Points dialog box
Import Points
Ribbon: Insert > Import > Points from File Command: IMPORTPOINTS

## Slide 22
POINT SETTINGS AND STYLES
Figure 2-18 Choosing the Edit Feature Settings option from the shortcut menu

## Slide 23
Figure 2-19 The Edit Feature Settings - Point dialog box

## Slide 24
Figure 2-20 Selecting the point style from the drop-down list
POINT STYLES
AutoCAD Civil 3D has some in-built point styles that control the visibility and appearance of Civil 3D points.
Control the visibility and display of points
Styles help you manage the workability of points.
Point styles can be assigned after the points are imported or created.

## Slide 25
Creating Point Styles
Figure 2-21 Choosing the New option from the shortcut menu
Invoke Point Style dialog box-
  Choose the Settings tab in the TOOLSPACE palette
  Expand the Point node
  Right-click on Point Styles
  Choose the New option from the shortcut
Figure2-22 Partial view of the Information tab of the Point Style - New Point Style dialog box

## Slide 26
Figure 2-23 The Marker tab in the Point Style - New Point Style dialog box

## Slide 27
POINT LABEL STYLES
Creating a Point Label Style
Figure 2-24 The options in the Layout tab
Point label styles control the behavior and appearance of point labels.
Point label styles are created and managed in the Settings tab of the Toolspace palette.

## Slide 28
Figure 2-25 The Component Draw Order dialog box
Use the Component Draw Order dialog box to specify the order in which label components will be displayed in the multi component label.
Choose the Component draw order button to invoke the Component Draw Order dialog box.

## Slide 29
Adding the Text Component to the Label
Figure 2-26 Choosing the browse button displayed in the Value field of the Contents property
Choose the Layout tab from the Label Style Composer dialog box
Choose the Create Text component button
Choose the browse button in the Value field of the Contents property, Text Component Editor dialog box will be displayed.
Figure 2-27 The Text Component Editor - Contents dialog box

## Slide 30
Figure 2-28 The Edit Label Style Defaults - Point dialog box
To view and edit the point label style settings-
Expand the Point node and right-click on the Label Styles sub-node in the Settings tab.
Choose Edit Label Style Defaults option from the shortcut menu; the Edit Label Style Defaults - dialog box will be displayed.

## Slide 31
EDITING POINTS
Ribbon: Modify > Ground Data > Points Command: EDITPOINTS
Figure 2-29 Choosing the Points tool from the Ground Data panel of the Modify tab
Renumbering a Point
Ribbon: COGO Point > Modify > Renumber
Command: SELECTANDEDITPOINTNUMBERS

## Slide 32
Changing the Elevation of the Point
Ribbon: COGO Point > Modify > Datum
Command: EDITPOINTDATUM
Changing the Point Elevation with respect to a Surface
Ribbon: COGO Point > Modify > Datum
Command: EDITPOINTSURFACEELEVS

## Slide 33
Figure 2-30 A red colored symbol displayed next to the locked point in the Point Editor tab
Locking/Unlocking Points
Ribbon: COGO Point > Modify > Lock Points/Unlock Points
Command: LOCK POINTS / UNLOCK POINTS

## Slide 34
Figure 2-31 The Geodetic Calculator dialog box
Using the Geodetic Calculator
Ribbon: COGO Point > Analyze > Geodetic Calculator
Command: SHOWGEODETICCALCULATOR

## Slide 35
Figure 2-32 The PANORAMA window with the Point Editor tab

## Slide 36
Importing Points
Ribbon: Home > Create Ground Data > Points drop-down
Command: IMPORTPOINTS
You can import points of various file formats into AutoCAD Civil 3D.
Use the Point Creation Tools tool to import points.
Choose the Import Points button from the Create Points toolbar; the Import Points dialog box is displayed.
You can import the required point file format using this dialog box .

## Slide 37
POINT GROUPS
Collection of similar points.
Point groups help you control, organize, and manage a point easily.
Points with similar properties such as description, elevation, and so on can be grouped together with a common point group name.
Like points, point groups also have their own styles and label styles.
You can assign different point styles and point label styles to each point group.

## Slide 38
Figure 2-33 The Point Group Properties - Point Group - (1) dialog box
Creating Point Groups
Ribbon: Home > Create Ground Data > Points drop-down > Create Point Group
Command: CREATEPOINTGROUP
Point groups are created based on point properties. You can group points based on their point numbers, elevation, description, and so on.
The options in the Point Group Properties dialog box are used to create point groups.

## Slide 39
Figure 2-34 The DescKey Editor in the Panorama window

## Slide 40
In this tutorial, you will create points using various tools that are available in the Create Points toolbar
Figure 2-35 Points created by using various tools in the Create Points toolbar
TUTORIALS
Tutorial 1 Creating Points I

## Slide 41
In this tutorial, you will import points into a drawing, create a point group, create a new point style, and a point label style for points, as shown in Figure 59.
Figure 2-36 Points created with a new point style and point label style
TUTORIALS
Tutorial 2 Importing Points

## Slide 42
In this tutorial, you will verify the drawing settings, create points manually using the coordinate data in latitude and longitude format, and create points using the Slope/Grade - Elevation tool, refer to Figure 2-37. .
Figure 2-37 Points created using the Slope/Grade - Elevation tool
TUTORIALS
Tutorial 3 Creating Points II